## Slide 1: U-boot
Raspberry pi 4B

## Slide 2: Content
Building
Flashing/Booting
Customize
Memory foot print Improvement
Secure boot

## Slide 3: Building
git clone https://gitlab.denx.de/u-boot/u-boot.git
cd u-boot
sudo apt-get install gcc-aarch64-linux-gnu
#!/bin/bash
pushd ~/Downloads/u-boot

## Slide 4: Building u-boot.bin
echo "changed to : " $(pwd)
make -j$(nproc) KBUILD_OUTPUT=build CROSS_COMPILE=aarch64-linux-gnu- rpi_4_defconfig
wait
make -j$(nproc) KBUILD_OUTPUT=build CROSS_COMPILE=aarch64-linux-gnu- all
wait

## Slide 5: Boot Script
pushd build
echo "chaned to : " $(pwd)
echo "creating a Boot script"
./tools/mkimage -A arm64 -T script -C none -n "Boot script" -d boot.scr boot.scr.uimg
wait
ls -lt u-boot.bin
ls -lt boot.scr.uimg
popd
echo "rpi 4 build finished " $(date)
popd

## Slide 6: Copy to SDCard: u-boot.bin & boot.scr.uimg
lsblk
sudo mount /dev/sdb1 /media/boot/
cp u-boot.bin /media/boot/
cp boot.scr.uimg media/boot/

## Slide 7: Enable u-boot loading by boootloader
nano /media/boot/config.txt
#Enable u-boot
kernel=u-boot.bin
sudo umount /media/boot
lsblk
Put SDCard to rpi & power on

## Slide 8: U-boot Shell
U-Boot 2023.01-rc4-00059-g8d6cbf5e6b (xxx xx 20xx - 14:41:38 +0100)
DRAM: 948 MiB (effective 1.9 GiB)
RPI 4 Model B (0xb03115)
Core: 209 devices, 16 uclasses, devicetree: board
MMC: mmcnr@7e300000: 1, mmc@7e340000: 0
Loading Environment from FAT... Unable to read "uboot.env" from mmc0:1...
In: serial
Out: serial
Err: serial
Net: eth0: ethernet@7d580000
PCIe BRCM: link up, 5.0 Gbps x1 (SSC)
starting USB...
Bus xhci_pci: Register 5000420 NbrPorts 5
Starting the controller
USB XHCI 1.00
scanning bus xhci_pci for devices... 2 USB Device(s) found
scanning usb for storage devices... 0 Storage Device(s) found
Hit any key to stop autoboot: 0
U-Boot> help

## Slide 9: U-Boot> version
U-Boot> version
U-Boot 2023.01-rc4-00059-g8d6cbf5e6b (xxx xx 20x - 14:41:38 +xx00)
aarch64-linux-gnu-gcc (Ubuntu 11.3.0-1ubuntu1~22.04) 11.3.0
GNU ld (GNU Binutils for Ubuntu) 2.38

## Slide 10: Issue: U-boot fails on booting compressed kernel Image
Hit any key to stop autoboot: 0
switch to partitions #0, OK
mmc0 is current device
Scanning mmc 0:1...
Found U-Boot script /boot.scr.uimg
218 bytes read in 17 ms (11.7 KiB/s)
## Executing script at 02400000
Working FDT set to 2eff2f00
8192917 bytes read in 373 ms (20.9 MiB/s)
kernel_comp_addr_r or kernel_comp_size is not provided!
SCRIPT FAILED: continuing...

## Slide 11: Solution 1: Update include/configs/rpi.h
--- a/include/configs/rpi.h
+++ b/include/configs/rpi.h
@@ -120,7 +120,10 @@
"scriptaddr=0x02400000\0" \
"pxefile_addr_r=0x02500000\0" \
"fdt_addr_r=0x02600000\0" \
- "ramdisk_addr_r=0x02700000\0"
+ "ramdisk_addr_r=0x02700000\0" \
+ "kernel_comp_addr_r=0x08E0000\0" \ (kernetl_adder_r + u-boot size)
+ "kernel_comp_size=0x0860000\0" (size of kernel)

## Slide 12: Solution 2: Or add env variable
Go to U-boot Shell
set env kernel_comp_addr_r 0x08E0000
set env kernel_comp_size 0x0860000
saveenv
reset

## Slide 13
U-Boot 2021.10 (0000 0000 - 00:x00:56 +0x00)
DRAM: 1.9 GiB
RPI 4 Model B (0xb03115)
MMC: mmcnr@7e300000: 1, mmc@7e340000: 0
Loading Environment from FAT... OK
In: serial
Out: vidconsole
Err: vidconsole
Net: eth0: ethernet@7d580000
PCIe BRCM: link up, 5.0 Gbps x1 (SSC)
starting USB...
Bus xhci_pci: Register 5000420 NbrPorts 5
Starting the controller
USB XHCI 1.00
scanning bus xhci_pci for devices... 2 USB Device(s) found
scanning usb for storage devices... 0 Storage Device(s) found
Hit any key to stop autoboot: 0
switch to partitions #0, OK
mmc0 is current device
Scanning mmc 0:1...
Found U-Boot script /boot.scr.uimg
218 bytes read in 16 ms (12.7 KiB/s)
## Executing script at 02400000
8192917 bytes read in 373 ms (20.9 MiB/s)
Uncompressing Kernel Image
Moving Image from 0x80000 to 0x200000, end=1820000
## Flattened Device Tree blob at 2eff2e00
Booting using the fdt blob at 0x2eff2e00
Using Device Tree in place at 000000002eff2e00, end 000000002f002feb
Starting kernel ...
Debian GNU/Linux 11 raspberrypi ttyS0
raspberrypi login:
U-boot Shell